MAGNUM

PRODUCT DESCRIPTION

The MAGNUM HDK is a completely hydraulic controlled high dump sweeper designed and manufactured by Eureka to sweep congested areas as well as large floor spaces.
It has a sweeping path of 1.250 mm and a cleaning capacity, at full speed, of 15.000 m²/h.

Hydraulically driven traction, container lift, main brush and vacuum fan, enable the Magnum clean the dirtiest floors very rapidly, and keep routine maintenance extremely simple, thus reducing downtime.

The multi-level-dump hopper, equipped with hydraulic flap, is located in the front of the machine, can be hydraulically raised up to 1.550 mm from the floor, and has a real volume capacity of 200 liters.

Magnum is equipped with a polyester bag filter, class USG, which is particularly efficient for the retaining of fine dust, and has a much longer lasting life than other traditional filters. It is anti-static, washable, and is equipped with a highly efficient dust filter-shaker which provides extreme cleaning without the need for filter removal.

The powerful Kubota ( three cylinders, 21 hp, liquid-cooled) engine grants maximum reliability and world-wide assistance. More horsepower and liquid cooled system allows for overall better performances, and longer lasting life.

The compactness of this sweeper, with its small turning radius (1.700 mm) makes it particularly suitable for sweeping in narrow, confined areas not accessible by larger machines, yet at a speed and productivity of much bigger sweepers.

POWER EFFICIENCY

- Fully hydraulic driven traction, container lift, main brush and vacuum fan, enable the new HDK clean the dirtiest floors very rapidly, and keep routine maintenance extremely simple, thus reducing downtime.

- More power allows for increased operational speed, which translates into increased productivity: an impressive 15.000 m²/h at full speed (12 km/h)!

- The structure is exceptionally strong to allow the machine to handle the toughest applications.

- The petrol version is also adapted for use with LPG. It will therefore be possible to work in both indoor and outdoor applications with the same machine.

MANEUVERABILITY EFFICIENCY

- The MAGNUM is particularly compact to allow for maximum maneuverability in narrow spaces.

- The speed is automatically decreased when the hopper is raised from the floor.

- The rear panels are rounded to allow for a better maneuverability when working close to walls. ( 1 )

- Large diameter wheels are fitted all round to allow for efficient work on uneven surfaces, to overcome slopes and to get onto pavements. ( 2 )

- The new rear tire is larger than the front ones to allow for a better grip to the floor.

- All wheels are of “full rubber” type, therefore you will not have to worry about checking air pressure or repair flats.

(1)                                                                (2)

FILTERING EFFICIENCY

Another major area of importance is the filtering system: most competitors machines offer a single panel filter system which has disadvantages such as rapid clogging, dust coming out from the filter seals, hardly removable dust and a small filtering area. Magnum is equipped with a two stage filtering system, it has a pre-filter system in the hopper, in addition, the Magnum is equipped as standard with a polyester bag filter, class USG, which is particularly efficient for the retaining of fine dust, and has a much longer lasting life than all other traditional filters. This means the Magnum has a unique filter system with a huge filter area, specifically designed to overcome dust emission problems.

- The hopper has been designed to separate and immediately retain the heavier particles of dust before they even reach the filters.

- A new, special metal gasket has been added along the filter sides, to completely enclose the filter stitches and retain the little amount of particles which could flow out from it.

WASTE COLLECTION EFFICIENCY

- Another area of importance is the position of the hopper.

The rear loading system offers better visibility and filling capacity than the front loading system, but large debris can not be picked up with the same efficiency. Also, the main brush wears more rapidly as it will have to rotate faster to throw debris in the rear hopper.

We have therefore developed a FRONT LOADING SYSTEM to allow for efficient pick up of heavy dirt, and have increased visibility by positioning the operator’s seat higher and more central than usual.  To add capacity, we have designed a 200 liters hopper, that can be hydraulically lifted up to 1.550 mm.

- Sweeper “trailing” is often a problem on some sweepers.  When the width of the main brush is greater than the width of the hopper, debris will go past the sides of the dirt container.  We have therefore designed a wide container which will handle the full volume of dirt thrown in by the main brush across the full widths.

- The hopper is actually floating on the floor, automatically adjusting to allow for easier pick up of larger waste.

- To enable the main brush ( 90 cm width ) to work on most floor types, we have designed a 3 section bristle brush.  Integrated in the same brush are: a fine bristle section for fine dust, a thicker bristle section for heavier dust, and a heavy bristle section for large debris. ( 1 )

- Furthermore, the main brush can be quickly replaced without tools.

- The main brush floats for better performance on uneven floors

- The brush pressure on the floor can be adjusted while working. This is done with a control positioned on the dashboard.

- The dirt container and the main brush are both equipped with new safety devices to decrease operational risks.

- New, special protection disks are now equipped to defend the main broom side flanges from damages associated to tangled ropes or excessive dust.

- The side brush (600 mm) is retractable with front\side anti-shocks, and has an adjustable pressure facility.  It can be replaced in a few seconds without tools.

(1)                                                             (2)

SERVICING EFFICIENCY

- All parts, motors, engines etc. are easily accessible for servicing, as side, upper and rear panels can be totally opened. (1)

- The rubber flaps are a wearing part on all sweepers: we designed the Magnum’s to be much thicker, and in such a way that they can be replaced in a few seconds without tools. (2)

- The main brush can be rapidly replaced without tools.

- All filters can be cleaned or replaced in a few seconds.

- The side brush can be rapidly replaced without tools.

- The hopper can be inspected and cleaned very easily thanks to an access door located in the front. (3)

- Batteries can be replaced easily and quickly thanks to a battery trolley mounted on wheels.  This slides out for ease of use.

(1)                                                           (2)                                                                (3)

MAJOR SELLING POINTS - SUMMARY

* STRONG METAL STRUCTURE

* LOW POWER CONSUMPTION

* HYDRAULIC DRIVE ON BOTH DIESEL AND PETROL VERSION

* EXCELLENT VISIBILITY

* 2 STAGES FILTERING SYSTEM ®

* LARGE POLYESTER FILTERING AREA

* FLOATING HOPPER

* MULTI-BRISTLE MAIN BRUSH, FLOATING

* PRESSURE OF MAIN BRUSH CAN BE ADJUSTED WHILE WORKING

* RAPID REPLACEMENT OF MAIN AND SIDE BRUSH

* RAPID REPLACEMENT OF FLAPS ®

* RETRACTABLE SIDE BRUSH

* VACUUM-FAN STOPS WHEN HOPPER IS LIFTED

* MAIN BRUSH AND DIRT CONTAINER EQUIPPED WITH NEW SAFETY DEVICES

* SPEED DECREASED WHEN HOPPER IS LIFTED

* LARGE DIAMETER TIRES

* FULL RUBBER TIRES

* EASY ACCESS FOR SERVICING

* ACCESS DOOR ON HOPPER

* EASY REPLACEMENT OF BATTERY TRAY ( OPTIONAL ON EB VERSION )

* MORE POWERFUL ENGINE (21 hp)

* VORTEX FILTER TO CLEAN VACUUM AIR INTAKE

COMPARISON CHARTS - 1. EUREKA MAGNUM VS RCM BOXER DIESEL and KÄRCHER 1550 B-D

| 1. MAJOR CHARACTERISTICS | MAGNUM HDK | RCM Boxer Diesel | KÄRCHER 1550 B-D | NOTES: |
| --- | --- | --- | --- | --- |
| Cleaning path with 1 side broom | mm 1250 | mm 1200 | mm 1250 | 1 |
| Cleaning path only main broom | mm 900 | mm 850 | mm 950 |  |
| Max speed | 12 Km\h | 11 Km\h | 10 km\h |  |
| Cleaning capacity at max speed | 15.000 m²\h | 13.200 m²\h | 12.500 m²\h | 2 |
| Capacity of dirt container ( volume ) | 200 l | 240 l | 180 l |  |
| Loading system | Front - hydraulic | Rear – hydraulic | Rear - hydraulic | 3 |
| Max. dumping height (hydraulically controlled) | mm 1.550 | mm 1.470 | mm 1.470 | 4 |
| Automatic speed limit when hopper is raised | YES | NO | NO | 5 |
| Access door on hopper | YES | NO | NO | 6 |
| Tilting hopper | YES | NO | NO | 7 |
| Width of hopper | Larger than main brush | - | Smaller than main brush | 8 |
| Gasket to seal hopper door | YES | NO | NO | 9 |
| Reinforcing metal flap on hopper | YES | NO | NO | 10 |
| Rapid replacement flaps | YES | NO | NO | 11 |
| Accessibility for servicing | Very good | OK | Good | 12 |
| 2. BRUSHES |  |  |  |  |
| Main brush drive | Hydraulic | Hydraulic | Hydraulic |  |
| Floating \ Self-leveling | YES | YES | YES |  |
| Self-adjusting | YES | YES | YES |  |
| Rapid replacement | YES | YES | YES |  |
| Multi-bristles main brush | YES - STANDARD | NO | NO | 13 |
| Adjustable pressure from operators position | YES | NO | NO | 14 |
| Side brush drive | Electric motor | Hydraulic | Hydraulic motor |  |
| Adjustable pressure from operators position | YES | NO | NO | 15 |
| Retractable | YES | YES | YES |  |
| Rapid replacement | YES | YES | NO | 16 |
| 3. FILTERING SYSTEM | MAGNUM HDK | RCM Boxer Diesel | KÄRCHER 1550 B-D | NOTES: |
| Type of filter | Polyester bag 452 KLEENTES, 450 g/m² - class L- USG | Polyester bag | Polyester round filter |  |
| Total filtering area | 6 m² | 9 m² | 12 m² |  |
| Composition | Polyester | Polyester | Polyester |  |
| Pre-filtering system in hopper | YES - METAL FLAP | NO | YES | 17 |
| Filter shaking system | Electric - Automatic | Electric - Manual | Electric - Manual | 18 |
| 4. DRIVE SYSTEM |  |  |  |  |
| Type of drive | Hydraulic drive on rear wheel. | Hydrostatic on front wheels | Hydraulic motor on front wheel |  |
| Type of wheels | Full rubber - non marking | Full rubber Front \ Pneumatic rear | Full rubber Front\rear |  |
| Turning radius | 1725 mm | ? | ? | 19 |
| 5. DIESEL ENGINE |  |  |  |  |
| Model | Kubota D 902 A Three cylinders Liquid cooled | Lombardini Two Cylinders Liquid cooled | Kubota D722-E Three cylinders Liquid cooled | 20 |
| Power | 20,6 hp ( at 3200 RPM ) | 13.,4 hp | 19 hp | 21 |

NOTES ON COMPARISON CHARTS - 1. EUREKA MAGNUM VS RCM BOXER DIESEL and KÄRCHER 1550 B-D

| NOTE NUMBER | FEATURE \ BENEFITS |
| --- | --- |
| 1\ 2 | The large main brush combined to a large sweeping path and a faster operational speed, allows for an overall larger working capacity and productivity. |
| 3 | Eureka designed a HYDRAULIC FRONT LOADING SYSTEM to allow for a more efficient pick up of larger debris and heavy dirt. Compared to the RCM and Kärcher system, we have increased visibility by positioning the operator’s seat at a higher and more central position. The rotation of the main brush is slower because it throws debris forward, this allows a minor bristle consumption of the main brush. |
| 4 \ 5 | Much easier maneuverability in occasion of dumping operations. |
| 6 | The hopper can be inspected and cleaned very easily thanks to an access door located in the front. The inspection door can also be used to load larger debris directly into the container. |
| 7 | The hopper is actually floating on the floor, automatically adjusting to allow for easier pick up of larger waste. |
| 8 | Sweeper "trailing" is often a problem on some sweepers. When the width of the main brush is greater than the width of the hopper, debris will go past the sides of the dirt container. We have therefore designed a wide container which will handle the full volume of dirt thrown in by the main brush across the full widths |
| 9 | While the hopper is being raised, some dust could fall out from the hopper’s door. To eliminate this problem, we have totally sealed with a rubber gasket the space between the hopper’s door and the hopper mouth. |
| 10 | This metal flap will better protect the hopper in case of collisions. |
| 11 | The rubber flaps are a wearing part on all sweepers: we designed the Magnum’s to be much thicker, and in such a way that they can be replaced in a few seconds without tools. |
| 12 | All parts, motors, engines etc. are easily accessible for servicing, as side, upper and rear panels can be totally opened. |
| 13 | To enable the main brush to work on most floor types, we have designed a 3 section bristle brush. Integrated in the same brush are: a fine bristle section for fine dust, a thicker bristle section for heavier dust, and a heavy bristle section for large debris. |
| 14\15 | Increased sweeping performances, easier and more comfortable control. |
| 16 | The side brush can be replaced in a few seconds without tools. Easier servicing. |
| 17 | Magnum is equipped with an pre-filter system in the hopper. This means the Magnum has a unique filter system with a huge filter area, specifically designed to overcome dust emission problems. |
| 18 | Magnum has been equipped with an automatic filter shaking system, once the engine is turned off the shaker automatically shakes the filter, this in case operator forgets to shake the filter at the end of the cleaning duty. |
| 19 | The steering wheel is free from motors, and thus can be turned at a wider angle. This allows for better maneuverability when working in narrow spaces. |
| 20\21 | Greater horse power and with the Kubota engine and Kubota is an international brand leader with world assistance. |

COMPARISON CHARTS - 2. EUREKA MAGNUM VS HAKO-JONAS 1450 V-D and TENNANT 6400 D

| MAJOR CHARACTERISTICS | MAGNUM HDK | Hako-Jonas 1450 V-D | TENNANT 6400 D | NOTES: |
| --- | --- | --- | --- | --- |
| Cleaning path with 1 side broom | mm 1250 | mm 1270 | mm 1270 |  |
| Cleaning path only main broom | mm 900 | mm 920 | mm 915 |  |
| Max speed | 12 Km\h | 10 Km\h | 9,6 Km\h | 1 |
| Cleaning capacity at max speed | 15.000 m²\h | 12.700 m²\h | 12.192 m²\h | 2 |
| Capacity of dirt container ( volume ) | 200 l | 250 l | 315 l theoretical – 189 l Real |  |
| Loading system | Front - hydraulic | Rear - hydraulic | Front - hydraulic | 3 |
| Max. dumping height (hydraulically controlled) | mm 1.550 | mm 1.520 | mm 1.525 | 4 |
| Automatic speed limit when hopper is raised | YES | NO | NO | 5 |
| Access door on hopper | YES | NO | YES | 6 |
| Tilting hopper | YES | NO | YES | 7 |
| Width of hopper | Larger than main brush | Smaller than main brush | Same width as main brush | 8 |
| Gasket to seal hopper door | YES | NO | YES | 9 |
| Reinforcing metal flap on hopper | YES | NO | YES | 10 |
| Rapid replacement flaps | YES | NO | NO | 11 |
| Accessibility for servicing | Very good | Good | Good |  |
| 2. BRUSHES |  |  |  |  |
| Main brush drive | Hydraulic | Hydraulic | Hydraulic |  |
| Floating \ Self-leveling | YES | Yes | YES |  |
| Self-adjusting | YES | Manual | YES | 12 |
| Rapid replacement | YES | YES | YES |  |
| Multi-bristles main brush | YES - STANDARD | NO | NO | 13 |
| Adjustable pressure from operators position | YES | YES | YES |  |
| Side brush drive | Electric motor | Hydraulic motor | Hydraulic motor |  |
| Adjustable pressure from operators position | YES | NO | ? | 14 |
| Retractable | YES | YES | YES |  |
| Rapid replacement | YES | YES | YES |  |

| 3. FILTERING SYSTEM | MAGNUM HDK | Hako-Jonas 1450 V-D | TENNANT 6400 D-B-E | NOTES: |
| --- | --- | --- | --- | --- |
| Type of filter | Polyester bag 452 KLEENTES, 450 g/m² - class L- USG | Panel | Panel | 15 |
| Total filtering area | 6 m² | 5,6 m² | 6,9 m² |  |
| Composition | Polyester | Polyester | Polyester |  |
| Pre-filtering system in hopper | YES - METAL FLAP | NO | YES | 16 |
| Filter shaking system | Electric - Automatic | Electric - Manual | Electric - Manual | 17 |
| 4. DRIVE SYSTEM |  |  |  |  |
| Type of drive | Hydraulic drive on rear wheel. | Hydraulic motor on front wheel | Hydraulic motor on rear wheel |  |
| Type of wheels | Full rubber - non marking | Full rubber | Pneumatic | 18 |
| Turning radius | 1725 mm | 2350 mm | 2360 mm | 19 |
| 6. DIESEL ENGINE |  |  |  |  |
| Model | Kubota D 902 A Three cylinders Liquid cooled | 2 cylinders Liquid cooled | Kubota Three cylinders Liquid cooled | 20 |
| Power | 20,6 hp ( at 3200 RPM ) | 14,5 hp | 26 hp |  |

NOTES ON COMPARISON CHARTS - 2.  EUREKA MAGNUM VS HAKO-JONAS 1450 V-D \ TENNANT 6400 D

| NOTE NUMBER | FEATURE \ BENEFITS |
| --- | --- |
| 1 \ 2 | The large main brush combined to a large sweeping path and a faster operational speed, allows for an overall larger working capacity. |
| 3 | Eureka designed a HYDRAULIC FRONT LOADING SYSTEM to allow for a more efficient pick up of larger debris and heavy dirt. Compared to Tennant’s system, we have increased visibility by positioning the operator’s seat at a higher and more central position. |
| 4 \ 5 | Much easier maneuverability in occasion of dumping operations. |
| 6 | The hopper can be inspected and cleaned very easily thanks to an access door located in the front. The inspection door can also be used to load larger debris directly into the container. |
| 7 | The hopper is actually floating on the floor, automatically adjusting to allow for easier pick up of larger waste. |
| 8 | Sweeper "trailing" is often a problem on some sweepers. When the width of the main brush is greater than the width of the hopper, debris will go past the sides of the dirt container. We have therefore designed a wide container which will handle the full volume of dirt thrown in by the main brush across the full widths |
| 9 | While the hopper is being raised, some dust could fall out from the hopper’s door. To eliminate this problem, we have totally sealed with a rubber gasket the space between the hopper’s door and the hopper mouth. |
| 10 | This metal flap will better protect the hopper in case of collisions. |
| 11 | The rubber flaps are a wearing part on all sweepers: we designed the Magnum’s to be much thicker, and in such a way that they can be replaced in a few seconds without tools. |
| 12 | The main brush automatically adjusts itself to the wear, thus increasing sweeping performances. |
| 13 | To enable the main brush to work on most floor types, we have designed a 3 section bristle brush. Integrated in the same brush are: a fine bristle section for fine dust, a thicker bristle section for heavier dust, and a heavy bristle section for large debris. |
| 14 | Increased sweeping performances, easier and more comfortable control. |
| 15 | Magnum is equipped with a polyester bag filter which is particularly efficient for the retaining of fine dust, and has a much longer lasting life than other traditional filters. Our competitor machines offer a panel filter system which has disadvantages such as rapid clogging and dust coming out from the filter seals |
| 16 | Magnum is equipped with an pre-filter system in the hopper. This means the Magnum has a unique filter system with a huge filter area, specifically designed to overcome dust emission problems. |
| 17 | Magnum has been equipped with an automatic filter shaking system, once the engine is turned off the shaker automatically shakes the filter, this in case operator forgets to shake the filter at the end of the cleaning duty. |
| 18 | All wheels are of "full rubber" and none marking type, therefore you will not have to worry about checking air pressure and leaving visible marks on the pavement or repair flats. Large diameter wheels are fitted all round to allow for efficient work on uneven surfaces, to overcome slopes and to get onto pavements. |
| 19 | The steering wheel is free from motors, and thus can be turned at a wider angle. This allows for better maneuverability when working in narrow spaces. |
| 20 | Kubota is an international brand leader with world assistance |

COMPARISON CHARTS - 3. EUREKA MAGNUM VS DULEVO 100 \ NILFISK SR 1450

| 1. MAJOR CHARACTERISTICS | MAGNUM HDK | DULEVO 100 | Nilfisk SR 1450 | NOTES: |
| --- | --- | --- | --- | --- |
| Cleaning path with 1 side broom | mm 1250 | mm 1350 | mm 1120 |  |
| Cleaning path only main broom | mm 900 | mm 1000 | mm 800 |  |
| Max speed | 12 km\h | 10,5 km\h | 13 Km\h |  |
| Cleaning capacity at max speed | 15.000 m²\h | 14.175 m²\h | 14.560 m²\h | 1 |
| Capacity of dirt container ( volume ) | 200 l | 236 l | 115 l | 2 |
| Loading system | Front - hydraulic | Front - hydraulic | Front - hydraulic |  |
| Max. dumping height (hydraulically controlled) | mm 1.550 | mm 1500 | mm 1.360 | 3 |
| Automatic speed limit when hopper is raised | YES | NO | NO | 4 |
| Access door on hopper | YES | NO | NO | 5 |
| Tilting hopper | YES | NO | NO | 6 |
| Width of hopper | Larger than main brush | Smaller then main brush | Smaller then main brush | 7 |
| Gasket to seal hopper door | YES | NO | NO | 8 |
| Reinforcing metal flap on hopper | YES | NO | NO | 9 |
| Rapid replacement flaps | YES | NO | YES | 10 |
| Accessibility for servicing | Very good | Very good | Standard |  |
| 2. BRUSHES |  |  |  |  |
| Main brush drive | Hydraulic | Hydraulic | Hydraulic |  |
| Floating \ Self-leveling | YES | YES | YES |  |
| Self-adjusting | YES | YES | YES |  |
| Rapid replacement | YES | YES | YES |  |
| Multi-bristles main brush | YES - STANDARD | NO | NO | 11 |
| Adjustable pressure from operators position | YES | YES | YES |  |
| Side brush drive | Electric motor | Hydraulic motor | Hydraulic motor |  |
| Adjustable pressure from operators position | YES | YES | YES |  |
| Retractable | YES | YES | YES |  |
| Rapid replacement | YES | NO | NO | 12 |
| 3. FILTERING SYSTEM | MAGNUM HDK | DULEVO 100 | Nilfisk SR 1450 | NOTES: |
| Type of filter | Polyester bag 452 KLEENTES, 450 g/m² - class L- USG | Polyester Bag | Polyester Bag |  |
| Total filtering area | 6 m² | 7,5 m² | 5,2 m² |  |
| Composition | Polyester | Polyester | Polyester |  |
| Pre-filtering system in hopper | YES - METAL FLAP | NO | NO | 13 |
| Filter shaking system | Electric - Automatic | Electric - Manual | Electric - Manual | 14 |
| 4. DRIVE SYSTEM |  |  |  |  |
| Type of drive | Hydraulic drive on rear wheel | Hydraulic motor on rear wheel | Hydraulic drive on rear wheel. |  |
| Type of wheels | Full rubber - non marking | Pneumatic | Full rubber | 15 |
| Turning radius | 1725 mm | ? | 2650 mm | 16 |
| 6. DIESEL ENGINE |  |  |  |  |
| Model | Kubota D 902 A Three cylinders Liquid cooled | Kubota Three cylinders liquid cooled | Lombardini 2 cylinders | 17 |
| Power | 20,6 hp ( at 3200 RPM ) | 24,5 hp | 13,4 hp |  |

NOTES ON COMPARISON CHARTS -3. EUREKA MAGNUM VS DULEVO 100 \ NILFISK SR 1450

| NOTE NUMBER | FEATURE \ BENEFITS |
| --- | --- |
| 1 | The large main brush combined to a large sweeping path and a faster operational speed, allows for an overall larger working capacity. |
| 2 | The capacity of the dirt container is larger than most competitors’, thus granting better productivity. |
| 3 \ 4 | Much easier maneuverability in occasion of dumping operations. |
| 5 | The hopper can be inspected and cleaned very easily thanks to an access door located in the front. The inspection door can also be used to load larger debris directly into the container. |
| 6 | The hopper is actually floating on the floor, automatically adjusting to allow for easier pick up of larger waste. |
| 7 | Sweeper "trailing" is often a problem on some sweepers. When the width of the main brush is greater than the width of the hopper, debris will go past the sides of the dirt container. We have therefore designed a wide container which will handle the full volume of dirt thrown in by the main brush across the full widths |
| 8 | While the hopper is being raised, some dust could fall out from the hopper’s door. To eliminate this problem, we have totally sealed with a rubber gasket the space between the hopper’s door and the hopper mouth. |
| 9 | This metal flap will better protect the hopper in case of collisions. |
| 10 | The rubber flaps are a wearing part on all sweepers: we designed the Magnum’s to be much thicker, and in such a way that they can be replaced in a few seconds without tools. |
| 11 | To enable the main brush to work on most floor types, we have designed a 3 section bristle brush. Integrated in the same brush are: a fine bristle section for fine dust, a thicker bristle section for heavier dust, and a heavy bristle section for large debris. |
| 12 | The side brush can be replaced in a few seconds without tools. Easier servicing. |
| 13 | Magnum is equipped with an pre-filter system in the hopper. This means the Magnum has a unique filter system with a huge filter area, specifically designed to overcome dust emission problems. |
| 14 | Magnum has been equipped with an automatic filter shaking system, once the engine is turned off the shaker automatically shakes the filter, this in case operator forgets to shake the filter at the end of the cleaning duty. |
| 15 | All wheels are of "full rubber" and none marking type, therefore you will not have to worry about checking air pressure and leaving visible marks on the pavement or repair flats. Large diameter wheels are fitted all round to allow for efficient work on uneven surfaces, to overcome slopes and to get onto pavements. |
| 16 | The steering wheel is free from motors, and thus can be turned at a wider angle. This allows for better maneuverability when working in narrow spaces. |
| 17 | Kubota is an international brand leader with world assistance |