## RIDER

PRODUCT DESCRIPTION

The Rider 1201 is a combination of technology and ideas which will enable the user to keep large areas clean, by working in total comfort, quickly and at low costs .

The wide sweeping path (1.210 mm) combined with the fast operational speed assures a large cleaning capacity (up to 9.680 m²\h); the compactness of this sweeper, with its small turning radius (1.050 mm), makes it particularly suitable for sweeping in narrow, confined areas not accessible by larger machines.

Fine dust is filtered through a polyester bag filter, which allows for an excellent filtering rate (99,9%) and has a much longer lasting life than traditional filters.

The floating, self-leveling main brush and the retractable, anti-shock side brushes allow the maximum cleaning efficiency on rough or uneven floors, while the large filter area enables sweeping in the dustiest of environments. This, in conjunction with a large debris container, reduces the wasted time, increasing overall productivity.

The hydrostatic drive on front wheel increases maneuverability and power and enables the Rider 1201 to operate on steep inclines.

The on-board vacuum cleaner enables the cleaning of edges and areas inaccessible to the main machine.

In addition, the original Italian touch is visible in the design of the external shapes: this adds an attractive appearance which is appreciated by customers all over the world.

After all, productive does not necessarily mean bulky.

SWEEPING / VACUUMING SYSTEM

- Rider 1201 has a main brush width of 700 mm, a total sweeping path of 1.210 mm and a cleaning capacity, at full speed, of 9.680 m²\h.

- The unit operates on the overthrow principle, i.e. debris are thrown over the cylindrical brush into the waste container situated behind it.

- The brush is suspended in floating mounts, so that it adjusts automatically to compensate for wear and uneven surfaces.

- A bulk waste flap is installed in front of the brush and easily opened from the driver's seat. It allows the broom to pick up even bulkier debris.

- Like the main brush, the standard right side brush is activated from the control panel. A second (left) side brush is available as an option. Both brushes are mounted on side shock-absorbers to prevent damages.

- The container has a real capacity of 85 Lt. It is equipped with wheels and has a convenient transport handle that allows the entire hopper to be rolled to the dump site.

- Visibility is excellent from the operator’s position, and all controls are simple and ergonomically located for easy operations.

- Maintenance access is convenient as well. The top lifts up to expose the engine or the battery compartment as well as motors and other service areas.

- Fine dust is filtered through a polyester bag filter, which allows for an excellent filtering rate (99,9%) and has a much longer lasting life than traditional filters. The filter can be cleaned thanks to an efficient electric filter-shaker.

- The on-board vacuum cleaner ( optional accessory, E version ) enables the cleaning of edges and areas inaccessible to the main machines.

MAJOR APPLICATIONS AND TARGET GROUPS

Thanks to its size, Rider 1201 is particularly suitable for the cleaning of outdoor large surfaces. It may also be suitable for a number of indoor applications and for the sweeping of large carpeted areas.

- Food industry

- Trucking and warehousing

- Paper and allied products

- Chemical industry

- Cleaning contractors

- Shopping malls

- Car parks

- Large hotel areas

- Lumber and wood products

- Service stations

- Airports ( indoor areas )

- Breweries

- Standard solid rubber tyres ( non-marking type ) allow unlimited operations in areas with glass or metal splinters.

- The floating main broom enables the Rider 1201 to work efficiently also on uneven floors.

- Working time on one battery charge is approx. 3 hours. This enables the Rider 1201 to sweep almost 29.040 m² (based on theoretical cleaning capacity) in a full working cycle.

STANDARD ACCESSORIES

* ELECTRIC ENGINE'S START , AUTOMOTIVE TYPE ( S VERSION )

* SYSTEM MOTOR 24V – 1200W ( E VERSION )

* POLYESTER BAG FILTER

* FLASHING LIGHTS

* CHEVRON TYPE MAIN BRUSH, IN PPL, MIXED BRISTLES, mm 700 x  285 mm

* RETRACTABLE RH SIDE BRUSH IN PPL, DIAMETER mm 500

* CENTRIFUGAL FRICTION ON ENGINE'S SHAFT FOR :

EASIER ENGINE'S START OPERATIONS , LOAD-FREE

LONGER LIFE FOR STARTING MOTOR

LONGER LIFE FOR BATTERY

* CONTROL PANEL INCLUSIVE OF :

STARTING KEY - ELECTRIC FILTER-SHAKER BUTTON

THROTTLE CONTROL - CHOKE CONTROL , HORN VACUUM CUT-OFF CONTROL

* FORWARD - REVERSE DRIVE HYDROSTATICALLY CONTROLLED

* SUPERELASTIC NON-MARKING TYRES

* BRAKES : HYDRAULIC SERVICE BRAKES , MECHANICAL PARKING BRAKES

* FLAP RAISING CONTROL FROM OPERATOR'S POSITION

* SELF-LEVELLING , SELF ADJUSTING CONTROL FOR MAIN BRUSH , POSSIBILITY TO ADJUST

THE BRUSH PRESSURE TO THE FLOOR , EXCELLENT ADHERENCE TO THE FLOOR ,

RAPID REPLACEMENT OF MAIN BRUSH , MIXED PPL BRISTLES.

* MAX SPEED 8 KM\H

* DUST CONTROL ON SIDE BRUSH

OPTIONAL ACCESSORIES

* RETRACTABLE LEFT SIDE BRUSH KIT

* CATALITYC CONVERTER KIT ( S VERSION )

* REFUSE BOXES KIT ( For dirt container )

* ACOUSTIC SIGNAL KIT ( reverse speed )

* PVC BUMPER KIT

* HOURMETER KIT

* CARPET CLEANING KIT

* ON-BOARD VACUUM CLEANER ( E VERSION )

* LOW CHARGE BATTERY ACOUSTIC SIGNAL  ( E VERSION )

* SPECIAL BAG FILTER “USGC” CLASS – COATED WITH POLYURETHAN

* ASTRO TURF KIT

FEATURES AND BENEFITS

POWER EFFICIENCY:

- HYDROSTATIC DRIVE ON FRONT WHEEL: The hydrostatic drive on front wheel increases maneuverability and power, thus enabling the machine to operate even on steep inclines.

MANEUVERABILITY EFFICIENCY:

- VERY COMPACT SIZE FOR MAXIMUM MANEUVERABILITY IN NARROW SPACES

- VERY LOW TURNING RADIUS: 105 cm

- SIMPLE CONTROLS: One pedal controls both forward and reverse speed. Main brush and side brush controls are conveniently located on the dashboard, as well as the vacuum-cut off device and the electric filter-shaker button.

- EXCELLENT VISIBILITY: The operator sits in front.

- Side brush(es) mounted on shock-absorbers:  additional protection against bumps or collisions.

- FULL RUBBER TIRES: You will not have to worry about checking air pressure or repair flats. Furthermore, wheels are of “non-marking” type as standard.

- PVC BUMPER: It offers additional protection against bumps or collisions.

WASTE COLLECTION EFFICIENCY:

- BACK LOADING SYSTEM: Thanks to the position of the hopper, the Rider 1201 offers better visibility and filling capacity.

- HOPPER MOUNTED ON WHEELS: It allows the hopper to be rolled to dump site without fatigue.

- MULTI-BRISTLES MAIN BRUSH: In order to enable the main brush ( 70 cm width ) to work on most floor types, we have designed a 2 sections bristle brush.  Integrated in the same brush are: a fine bristle section for fine dust and a thicker bristle section for heavier dust.

- FLOATING, SELF-ADJUSTING MAIN BRUSH: The main brush floats for better performances on uneven floors, and automatically adjusts itself to compensate for wear and uneven surfaces.

- ON-BOARD VACUUM-CLEANER: The on-board vacuum cleaner (optional accessory, E version) enables the cleaning of edges and areas inaccessible to the main machines.

USER FRIENDLY:

- ALL CONTROLS LOCATED AT DRIVER’S REACH: The main brush/ side brush(es) can be lowered or raised from the floor thanks to a lever positioned on the dashboard.

- ADJUSTABLE SEAT: For extra operator’s comfort.

- VACUUM-FAN CUT-OFF: It allows the machine to work efficiently also on wet areas.

- STRONG METAL STRUCTURE, COATED WITH EPOXY POWDER: Additional protection against bumps, collisions, and better protection against scratches or rust.

- EASY ACCESS FOR SERVICING: The top lifts up to expose the battery compartment as well as motors and other service areas.

- VERY COMPETITIVE PRICE!!

COMPARISON CHART: RIDER 1201 SH vs. ISAL PB 111 SH – NILFISK SR1101 S – HAKO JONAS 950

| MAJOR CHARACTERISTICS | RIDER 1201 SH | ISAL PB 111 SH | NILFISK SR1101 S | HAKO JONAS 980 |
| --- | --- | --- | --- | --- |
| Cleaning path with 2 side brooms | mm 1210 | mm 1200 | mm 1260 | mm 1200 |
| Cleaning path with 1 side broom | mm 1070 | mm 950 | mm 980 | mm 950 |
| Cleaning path only main broom | mm 700 | mm 700 | mm 700 | mm 700 |
| Max. cleaning capacity | 9,680 m²/h | 7.500 m²/h | 6.300 m²/h | 7,200 m²/h |
| Forward speed | 8,45 Km\h | 6,4 Km/h | 5 Km\h | 0 - 6 Km/h |
| Capacity of dirt container | 85 l | 65 l | 70 l | 60 l |
| Turning radius | 1050 mm | - | 2380 mm | - |
| ENGINE |  |
| Model | Honda | Honda | Honda | Kawasaki |
| Rated Power | 6.5 HP | 6 HP | 3,9 HP | - |
| FILTERING SYSTEM |  |  |  |  |
| Type of filter | Bag filter | Panel | Panel | Panel |
| Number of filters | 1 | 1 | 1 | 1 |
| Total filtering area | 2,5 m² | 6 m² | 3,6 m² | 3 m² |
| Composition of standard filter | Polyester | Cellulose fiber | Cellulose fiber | Cellulose fiber |