## E36

Product description

The model E36 is a walk-behind professional scrubber-dryer, ideal for the cleaning of surfaces between 0 m² and 550 m².

With a cleaning width of 360mm and a speed of 3,5 km/h, this model boasts an area coverage of 1.100 m²/h.

Available either cable and battery powered.

Here below, the most important characteristics of this model:

- Strong anti-corrosion structure guaranteed for several years ;

- Automatic brush connection system without tools;

- Tanks capacity : 14/ 16 litres;

- Parabolic squeegee with double regulation equipped with LINATEX blades to ensure excellent drying;

- Powerfully scrub around obstacles with its maneuverable handle;

- Easy accessible tanks offer remarkable ease of filling, emptying and cleaning, even in the most awkward locations.

- Ergonomic handles and grips eliminate weariness and boost operator satisfaction.

BRUSH AND SQUEEGEE

- The E36 has a cleaning width of 360 mm, a squeegee width of 450 mm and an area coverage of 1.332 m²\h.

- The brush pressure is fixed (26Kg).

- The brush, or the abrasive pad, can be rapidly replaced without tools.

- Connecting pipe between the solution tank and brush head attached directly to the chassis, it prevents accidentals ruptures.

- The parabolic squeegee with a double adjustment is equipped with PARA blades in order to grant an excellent drying.

Applications

It’s indicated to clean all paved surfaces, internal and external like : ceramic tiles, marble, cement, linoleum, porcelain tiles, rubber floors on any kind of dirt.

- Small factories

- Restaurants

- Schools

- Kitchens

- Hospitals

- Locker rooms

- Cleaning companies

- Supermarkets

standard ACCESSORIES

- ON BOARD BATTERY CHARGER

- AUTOMATIC DRIVE

- AUTOMATIC BRUSH COUPLING

- BATTERY CHARGE INDICATOR WITH SAFETY POWER CUT-OFF

- iNCLINATION AND PRESSURE ADJUSTMENT

- 12V - 80A BATTERY

- ppl brush

OPTIONAL ACCESSORIES

- PAD HOLDER

- ABRASIVE DISC

TRACTION

The E36 has a mechanical traction

BATTERY CHARGER

The battery charger is available as standard accessory on the E36.

To charge the battery, it’s enough to connect the cable to a 220V outlet when the machine is turned off. In case the operator forgets to turn off the machine before the charge, an automatic device will turn it off once the cable is connected to the outlet and i twill automatically turn it on once on unplug the cable.

POWER

The E36 is available :

  - Cable powered

2.  Battery powered

ASPIRATION ENGINE

The 12V – 200W/ 230V – 200W aspiration engine, creates a vacuum of 700 mm / H20.

TANKS

The tanks are 2: the solution tank (14L) and the recuperation tank (16L).

The special design of the recuperation tank and the emptying, large diameter, pipe, allow to completely empty the dirty water, IN A VERY SHORT TIME,  without leaving any kind of rest and without manual intervention.

COMPARISON SHEET – E36B vs COMAC VISPA 35B and FIMAP GENIE B

| MAIN characteristics | E36B | COMAC VISPA 35B | FIMAP GENIE B | NOTES |
| --- | --- | --- | --- | --- |
| Cleaning width | 360mm | 350mm | 350mm | 1 |
| Squeegee width | 450mm | 450mm | 450mm | 2 |
| Brush pressure | 26kgs | 20kgs | 20kgs | 3 |
| Weight machine naked | 37kgs | 42kgs | 42kgs |  |
| Area coverage | 1100 m²/h | 1000 m²/h | 1000 m²/h | 1 |
| Climbing rate | 2% | 2% | 2% |  |
| N° of brushes | 1 | 1 | 1 |  |
| Tanks capacity | 14 l – 16 l | 10 l – 10 l | 10 l – 10 l | 4 |
| Noise level | 72dB | 69dB | 69dB |  |
| Water flow (l/m) | 0,40 | - | - | 3 |
| Total power | 450W | 610W | 610W |  |
| Automatic brush connection system | Yes | No | No | 6 |
| Rpm brushes | 140 | 140 | 140 | 3 |
| Speed (km/h) | 3,5 | 2,8 | 2,8 | 1 |
| On board charger | Yes | Yes | Yes |  |
| Vacuum | 700 mm/H²O | - | - | 2 |
| Autonomy | 1H40 | 1H00 | 1H00 | 5 |

COMPARISON SHEET – E36B vs COMAC VISPA 35B and FIMAP GENIE B

| NOTE N.RO | FEATURES/ADVANTAGES |
| --- | --- |
| 1 | The cleaning width combined with an higher working speed, allows a bigger productivity. |
| 2 | An optimum squeegee width combined with a great air depression, allows a perfect floor drying. |
| 3 | The right brush pressure combined with an excellent RPM and a bigger water flow grants a prefect results without efforts. |
| 4 | A bigger tank capacity grants an higher working autonomy with an impressive labor costs saving. |
| 5 | A bigger battery autonomy grants a bigger working autonomy with an impressive labor costs saving. |
| 6 | Automatic brush connection system it’s an indispensable option to speed up the work and simplify the usage of the machine. |

COMPARISON SHEET – E36B vs HAKO B12 and NILFISK SC351

| MAIN characteristics | E36B | HAKO B12 | NILFISK SC351 | NOTES |
| --- | --- | --- | --- | --- |
| Cleaning width | 360mm | 380mm | 370mm | 1 |
| Squeegee width | 450mm | 470mm | 475mm | 2 |
| Brush pressure | 26kgs |  | 27kgs | 3 |
| Weight machine naked | 37kgs | 40kgs | 42kgs |  |
| Area coverage | 1100 m²/h | 1500 m²/h | 890 m²/h | 1 |
| Climbing rate | 2% | 2% | 2% |  |
| N° of brushes | 1 | 1 | 1 |  |
| Tanks capacity | 14 l – 16 l | 16 l – 22 l | 11 l – 11 l | 4 |
| Noise level | 72dB |  | 64dB |  |
| Water flow (l/m) | 0,40 | - | 0,25 | 3 |
| Total power | 450W | 540W | 910W |  |
| Automatic brush connection system | Yes | Yes | Yes | 6 |
| Rpm brushes | 140 |  | 140 | 3 |
| Speed (km/h) | 3,5 | 4 | 4 | 1 |
| On board charger | Yes | Yes | Yes |  |
| Vacuum | 700 mm/H²O | - | - | 2 |
| Autonomy | 1H40 | 0H55 | 1H15 | 5 |

COMPARISON SHEET – E36B vs HAKO B12 and NILFISK SC351

| NOTE N.RO | FEATURES/ADVANTAGES |
| --- | --- |
| 1 | The cleaning width combined with an higher working speed, allows a bigger productivity. |
| 2 | An optimum squeegee width combined with a great air depression, allows a perfect floor drying. |
| 3 | The right brush pressure combined with an excellent RPM and a bigger water flow grants a prefect results without efforts. |
| 4 | A bigger tank capacity grants an higher working autonomy with an impressive labor costs saving. |
| 5 | A bigger battery autonomy grants a bigger working autonomy with an impressive labor costs saving. |
| 6 | Automatic brush connection system it’s an indispensable option to speed up the work and simplify the usage of the machine. |