## E50/ E55

PRODUCT DESCRIPTION

The models E50 and E55 are professional walk-behind scrubber-dryers, ideals for the cleaning of surfaces between 250 m² and 2.000 m².

With a cleaning width of 500mm and 550 mm and a speed of 4,3 km/h, these models boast an area coverage of 2.200 m²/h.

Here after, the most important characteristics of this model:

- Strong anti-corrosion structure guaranteed several years;

- ESCS (Eureka Solution Control Stop-Valve) cuts off or activates the flow of solution upon brush command (standard on Trac version);

- Adjustable brushing head for an optimal traction stability on all type of floors;

- Adjustable solution flow;

- Parabolic squeegee with a double adjustment, equipped with LINATEX blades to grant a perfect drying;

- EDS (Eureka Dosing System) on board detergent dosing system (optional);

- Anti foam device;

- Electronic traction (optional).

The models 50 and 55 are available in the BASE and TRAC versions and can be equipped with several available options.

BRUSHES AND SQUEEGEE

- The E50 and E55 have a cleaning width of 500 and 550mm, a squeegee width of 830 mm and boast an area coverage of 2.000 – 2.200 m²\h.

- The brush pressure is fixed (31Kg for the E50 and 43,50 for the E55).

- An electromagnetic valve (optional) starts the water flow slightly before the rotation of the brush or pad.

- Adjusting knob: to adjust the brush angle thus counterbalancing the sense of direction of the machine.

- Brush connection: the brush can be quickly connected/ disconnected without need for tools.

- Brush engine: direct drive to the brush (no belt).

- Brushing die cast aluminium  head equipped with protection wheels.

- Brushing Head adjusting handle.

- The parabolic squeegee with double adjustment is equipped with LINATEX blades in order to grant an excellent drying.

Applications

It is suitable to clean all paved floors, internal and external like: ceramic tiles, marble, cement, linoleum, porcelain tiles and with any kind of dirt.

- Factories

- Communities

- Schools

- Churches

- Hospitals

- Swimming pools

- Airports

- Locker rooms

- Commercial centres

- Logistic centres

- Cleaning companies

- Restaurants

Standard ACCESSORIES

- ON-BOARD BATTERY CHARGER

- NO TOOLS, easy BRUSH COUPLING SYSTEM

- ADJUSTABLE PRESSURE AND INCLINATION SQUEEGEE

- SELF-LEVELING BRUSH DECK SEALING RUBBER

- BATTERY CHARGE INDICATOR WITH SAFETY POWER CUT-OFF

- SUPERELASTIC, NON-MARKING REAR TYRES

- WATER FLOW DOSING

OPTIONAL ACCESSORIES

- WET TUBOLAR BATTERIES 12V – 105 AH

- AGM BATTERIES 12V – 90 AH

- BRUSH IN PPL 0,9 – 0,6

- PAD HOLDER

- ABRASIVE BRUSH 1,2

- INOX SQUEEGEE (without blades)

- HOURMETER

- DETERGENT DOSING SYSTEM

- ESCS (Eureka Solution Control Stop Valve)

TRACTION

The E50/ E55 use the following types of traction:

- Mechanical traction, available with the BASE version (operated by the rotation of the brush)

- The version Trac (the traction is ELECTRONIC, with a variable control)

BATTERY CHARGER

The batteries charger is a standard equipment on these models.

To charge the batteries just plug the cable into an outlet of 220V with the machine off. It is better to turn off the machine before making this type of operation, if it was not the case, a safety mechanism automatically shut off the machine when inserting the plug and then it will turn it on once the plug is disconnected.

POWER SUPPLY

The E51 is available with the following batteries (optional):

  - AGM batteries : 2 x 12V (90 AH)

- they don’t need maintenance

- there is no exhalation gas during loading

- there is no acid dispersion

-    they are completely sealed (there is no hole for inspection)

2.  Wet batteries: 2 x 12V (105 AH)

The machine can be adapted to any kind of battery simply changing the charging type in the battery charger.

VACUUM ENGINE

The 2 stages vacuum engine, 24V - 400W – 14/15 AH creates a depression of 1183 mm/ H20.

TANKS

The tanks are 2 : the solution tank (40L) and the recovery tank (50L).

The special design of the recovery tank and the big diameter draining pipe allow to empty completely the dirty water, IN A VERY SHORT TIME, without leaving any type of rest and without manual interventions.

COMPARISON SHEET – E50 base vs FIMAP MY 50 and NILFISK SC450B

| MAIN FEATURES | E50 | FIMAP MY 50 | NILFISK SC450B |
| --- | --- | --- | --- |
| Cleaning width | 500mm | 510mm | 530mm |
| Squeegee width | 830mm | 680mm | 760mm |
| Brush pressure | 31kgs | 27,50kgs | 34kgs |
| Naked machine weight | 73kgs | 62kgs | 76kgs |
| Productivity | 1.500 m²/h | 1.600 m²/h | 1.590 m²/h |
| Climbing rate | 3% | 2% | 2% |
| Brushes n° | 1 | 1 | 1 |
| Tanks capacity | 40 l – 50 l | 40 l – 40 l | 40 l – 45 l |
| Noise level | 73dB | - | 68dB |
| Water flow (l/m) | 0-2,3 | - | 0-1,8 |
| Rated power | 1.000W | 870W | 810W |
| Easy brush connection | Yes | Yes | Yes |
| Rpm brushes | 180 | 135 | 154 |
| Speed (km/h) | 3 | 3 | 3 |
| On board charger (standard) | Yes | No | No |
| Water lift | 1.183 mm/H²O | - | - |
| Brush engine rated power | 600 W | 560 W | - |
| Vacuum engine rated power | 400 W | 310 W | - |
| Autonomy (with 24V 90 Ah Gel battery) | 3H15 | 2H | 2H15 |

COMPARISON SHEET – E50 base vs COMAC L20 and RCM GO 531

| MAIN FEATURES | E50 | COMAC L20 | RCM Go 531 |
| --- | --- | --- | --- |
| Cleaning width | 500mm | 510mm | 530mm |
| Squeegee width | 830mm | 680mm | 745mm |
| Brush pressure | 31kgs | 27,50kgs | - |
| Naked machine weight | 73kgs | 62kgs | 68kgs |
| Productivity | 1.500 m²/h | 1.600 m²/h | 1.590 m²/h |
| Climbing rate | 3% | 2% | 2% |
| Brushes n° | 1 | 1 | 1 |
| Tanks capacity | 40 l – 50 l | 40 l – 40 l | 45 l – 48 l |
| Noise level | 73dB | - | - |
| Water flow (l/m) | 0-2,3 | - | - |
| Rated power | 1.000W | 870W | 1.000W |
| Easy brush connection | Yes | Yes | Yes |
| Rpm brushes | 180 | 135 | - |
| Speed (km/h) | 3 | 3 | 3 |
| On board charger (standard) | Yes | No | No |
| Water lift | 1.183 mm/H²O | - | - |
| Brush engine rated power | 600 W | 560 W | - |
| Vacuum engine rated power | 400 W | 310 W | - |
| Autonomy (with 24V 90 Ah Gel battery) | 3H15 | 2H | 1H45 |

COMPARISON SHEET – E55 base vs FIMAP MY50 B and RCM GO 552

| MAIN FEATURES | E55 | FIMAP MY 50 B | RCM Go 552 |
| --- | --- | --- | --- |
| Cleaning width | 550mm | 550mm | 540mm |
| Squeegee width | 830mm | 780mm | 745mm |
| Brush pressure | 43kgs | 27,50kgs | - |
| Naked machine weight | 78,50kgs | 62kgs | 73kgs |
| Productivity | 1.650 m²/h | 1.650 m²/h | 1.620 m²/h |
| Climbing rate | 3% | 2% | 2% |
| Brushes n° | 1 | 1 | 2 |
| Tanks capacity | 40 l – 50 l | 40 l – 40 l | 45 l – 48 l |
| Noise level | 73dB | - | - |
| Water flow (l/m) | 0-2,3 | - | - |
| Rated power | 1.150W | 870W | 800W |
| Easy brush connection | Yes | Yes | Yes |
| Rpm brushes | 150 | 135 | - |
| Speed (km/h) | 3 | 3 | 3 |
| On board charger (standard) | Yes | No | No |
| Water lift | 1.183 mm/H²O | - | - |
| Brush engine rated power | 750 W | 560 W | - |
| Vacuum engine rated power | 400 W | 310 W | - |
| Autonomy (with 24V 90 Ah Gel battery) | 2H25 | 2H | 2H15 |

COMPARISON SHEET – E55 base vs COMAC L22 and NUMATIC TTB 4055

| MAIN FEATURES | E55 | COMAC L22 | NUMATIC TTB 4055 |
| --- | --- | --- | --- |
| Cleaning width | 550mm | 550mm | 550mm |
| Squeegee width | 830mm | 780mm | - |
| Brush pressure | 43kgs | 27,50kgs | - |
| Naked machine weight | 78,50kgs | 62kgs | - |
| Productivity | 1.650 m²/h | 1.650 m²/h | 1.650 m²/h |
| Climbing rate | 3% | 2% | 2% |
| Brushes n° | 1 | 1 | 1 |
| Tanks capacity | 40 l – 50 l | 40 l – 40 l | 40 l – 40 l |
| Noise level | 73dB | - | 69 dB |
| Water flow (l/m) | 0-2,3 | - | 0-2 |
| Rated power | 1.150W | 870W | 800W |
| Easy brush connection | Yes | Yes | Yes |
| Rpm brushes | 150 | 135 | 100 |
| Speed (km/h) | 3 | 3 | 3 |
| On board charger (standard) | Yes | No | No |
| Water lift | 1.183 mm/H²O | - | - |
| Brush engine rated power | 750 W | 560 W | 400 W |
| Vacuum engine rated power | 400 W | 310 W | 400 W |
| Autonomy (with 24V 90 Ah Gel battery) | 2H25 | 2H | 2H15 |