## E71

PRODUCT DESCRIPTION

The model E71 it’s a professional walk-behind scrubber-dryer, ideal for the cleaning of surfaces between 2.000 m² and 3.000 m².

With a cleaning width of 710mm and a speed of 4,5 km/h, this model boasts an area coverage of 3.150 m²/h.

The ECO system (patented) is characterized by a device that grants an economy of either water and detergent. The ECO system has already won various prizes (like the one issued by Veneto Sviluppo – University of Padova).

The system, created to grant impressive savings of work/ water/ detergent, grants a productivity 4 times bigger than the traditional systems.

Here after, the most important characteristics of this model:

- Strong anti-corrosion structure guaranteed several years;

- The exclusive BRUSH‘OMATIC system for rapid replacement of either brushes and pads without tools;

- Adjustable solution flow proportional to the speed of the machine;

- Parabolic squeegee with a double adjustment, equipped with LINATEX blades to grant a perfect drying;

- Auto adjusting splash skirts to optimize the work on all type of floors;

- Electronic traction, infinitely variable.

The model E71 is available in the TRAC and ECO versions.

BRUSHES AND SQUEEGEE

- The E71 has a cleaning width of 710 mm, a squeegee width of 995 mm and boasts an area coverage of 3.195 m²\h.

- The brush pressure is 43kgs and 57kgs.

- An electromagnetic valve starts the water flow slightly before the rotation of the brush or pad.

- The exclusive BRUSH‘OMATIC system  (automatic brush connection) grants a very fast brush replacement.

- Automatic water flow system: thanks to this system, the solution flow is proportional to the machine speed.

- Brushing die cast aluminium  head equipped with protection wheels.

- The parabolic squeegee with double adjustment is equipped with LINATEX blades in order to grant an excellent drying.

- Filter dust class M (USGC): situated in the internal part of the tank, it protects the aspiration engine from eventual hazardous waste and dust.

- Eco System device: it is a system that maximize the productivity of the machine boasting to the maximum the efficacy of the cleaning solution (* SEE NOTES).

* THE EXCLUSIVE ECO-SYSTEM:

It is an exclusive device that, maximizing the use of the detergent solution, maximize the productivity of the machine.

In fact, with a standard machine, once the detergent solution is over, the operator will have to empty the recuperation tank and to fill the solution’s one. This leads inevitably to a loss in terms of: detergent solution, time and productivity – and also to negative consequences for the environment.

Eureka, contrary, offers a unique system for the utilization of the detergent solution with the objective to increase the working autonomy and to reduce the necessary time for the filling and the emptying of the tanks – reducing also the quantity of water and detergent necessary for the cleaning, and avoiding a productivity and labor loss.

Applications

It is suitable to clean all paved floors, internal and external like: ceramic tiles, marble, cement, linoleum, porcelain tiles and with any kind of dirt.

- Factories

- Communities

- Schools

- Churches

- Hospitals

- Swimming pools

- Airports

- Locker rooms

- Commercial centres

- Logistic centres

- Cleaning companies

- Restaurants

Standard ACCESSORIES

- IP54 ON-BOARD BATTERY CHARGER

- WATER CUT-OFF ELECTROVALVE WHEN MACHINE IS TURNED OFF

- CLEAN WATER SAFETY FILTER

- STAINLESS STEEL FILTER

- NO TOOLS, AUTOMATIC BRUSH COUPLING SYSTEM

- ADJUSTABLE PRESSURE AND INCLINATION SQUEEGEE

- SELF-LEVELING BRUSH DECK SEALING RUBBER

- PARKING BRAKE ON BOTH REAR WHEELS

- HOURMETER

- BATTERY CHARGE INDICATOR WITH SAFETY POWER CUT-OFF

- EMERGENCY STOP BUTTON

- SUPERELASTIC, NON-MARKING REAR TYRES

- DEAD MAN SAFETY BUTTON

- WATER FLOW PROPORTIONAL WITH THE SPEED OF THE MACHINE

- WATER FLOW DOSING BY A +/- BUTTONS SYSTEM

- EXCLUSIVE DEVICE « ECO SYSTEM »

OPTIONAL ACCESSORIES

- WET TUBOLAR BATTERIES 6V – 180 AH

- GEL BATTERIES 6V – 180 AH

- 2 X BRUSHES PPL 0,6

- 2 X BRUSHES PPL 0,9

- 2 X PAD HOLDER

- 2 X ABRASIVE BRUSHES 1,2

- INOX SQUEEGEE (without blades)

- SST (Stainless Steel Version)

TRACTION

The E71 uses the following types of traction:

- The versions Trac/Eco (the traction is ELECTRONIC, with an infinitely variable control)

BATTERY CHARGER

The batteries charger is a standard equipment on the two versions.

To charge the batteries just plug the cable into an outlet of 220V with the machine off. It is better to turn off the machine before making this type of operation, if it was not the case, a safety mechanism automatically shut off the machine when inserting the plug and then it will turn it on once the plug is disconnected.

POWER SUPPLY

The E71 is available with the following batteries (optional):

  - Gel batteries: 4 x 6V (180 AH)

- they don’t need maintenance

- there is no exhalation gas during loading

- there is no acid dispersion

-    they are completely sealed (there is no hole for inspection)

2.  Traditional batteries: 4 x 6V (180 AH)

The machine can be adapted to any kind of battery simply changing the charging type in the battery charger and the settings in the electronic card.

ASPIRATION ENGINE

The aspiration engine 24V - 550W – 25 AH creates a depression of 1250 mm/ H20.

TANKS

The tanks are 2 : the solution tank (70L) and the recovery tank (80L).

The special design of the recovery tank and the big diameter draining pipe allow to empty completely the dirty water, IN A VERY SHORT TIME, without leaving any type of rest and without manual interventions.

COMPARISON SHEET – E71 vs NILFISK BA 725 and IPC CT 70 BT 70

| MAIN FEATURES | E71 | NILFISK BA 725 | IPC CT 70 BT 70 | NOTES |
| --- | --- | --- | --- | --- |
| Cleaning width | 710mm | 710mm | 700mm | 1 |
| Squeegee width | 995mm | 930mm | 1010mm | 2 |
| Brush pressure | 43-57kgs | 36-59-73kgs | - | 3 |
| Naked machine weight | 173kgs | 197kgs | 94,5kgs |  |
| Productivity | 3195 m²/h | 3000 m²/h | 3150 m²/h | 1 |
| Climbing rate | 20% | 2% | 2% | 5 |
| Brushes n° | 2 | 2 | 2 |  |
| Tanks capacity | 70 l – 80 l | 76l – 76l | 70 l -75 l |  |
| Aspiration filter in class M | Yes ( in class M) | Yes | Yes | 4 |
| Noise level | 63dB | 87,6dB | 67dB | 6 |
| Water flow (l/m) | 1-5 | 0,95 – 1,9 – 2,8 | - | 3 |
| Rated power | 1.970W | 1.610W | 1.080W |  |
| Automatic splash skirts | Yes | No | No |  |
| Automatic brush connection | Yes | No | No | 7 |
| Reverse speed | Yes | Yes | Yes |  |
| Rpm brushes | 200 | 220 | 215 | 3 |
| Brakes | Yes | No | No |  |
| Speed (km/h) | 4,5 – 1,5 | 4,8 | 4,5 | 1 |
| On board charger | Yes | No | No |  |
| Water lift | 1250 mm/H2O | - | - | 2 |

COMPARISON SHEET – E71 vs NILFISK BA 725 and IPC CT 70 BT 70

| NOTE N. | FEATURES / BENEFITS |
| --- | --- |
| 1 | The cleaning width combined to an higher working speed, allows a bigger productivity. |
| 2 | An optimal squeegee width combined to an excellent water lift, allow a impeccable floor drying. |
| 3 | The right brush pressure combined to an excellent RPM and a bigger water flow grant an excellent floor cleaning without efforts. |
| 4 | The aspiration engine class M filter protects it from damages due to the powder, reducing the maintenance. |
| 5 | A better climbing rate grants a more comfortable use in any kind of location. Either during the usage of the machine either during its transportation. |
| 6 | With its incredibly low noise level, the E71 is the ideal machine to work in any kind of location at any time. |
| 7 | The automatic brushes connection is an essential option to accelerate the cleanup and facilitate the use of the machine. |

COMPARISON SHEET – E71 vs TENNANT T5 and FIMAP SMX 75 BT

| MAIN FEATURES | E71 | TENNANT T5 | FIMAP SMX 75 BT | NOTES |
| --- | --- | --- | --- | --- |
| Cleaning width | 710mm | 700mm | 760mm | 1 |
| Squeegee width | 995mm | 1050mm | 1050mm | 2 |
| Brush pressure | 43-57kgs | 18-36-54 | 30-50kgs | 3 |
| Naked machine weight | 173kgs | 165kgs | 160kgs |  |
| Productivity | 3195 m²/h | 2800 m²/h | 3300 m²/h | 1 |
| Climbing rate | 20% | 8% | 10% | 5 |
| Brushes n° | 2 | 2 | 2 |  |
| Tanks capacity | 70 l – 80 l | 85l – 102l | 80 l – 90 l |  |
| Aspiration filter in class M | Yes ( in class M) | Yes | Yes | 4 |
| Noise level | 63dB | 67dB | - | 6 |
| Water flow (l/m) | 1-5 | - | - | 3 |
| Rated power | 1.970W | 1.930W | - |  |
| Automatic splash skirts | Yes | Yes | Yes |  |
| Automatic brush connection | Yes | No | No | 7 |
| Reverse speed | Yes | Yes | Yes |  |
| Rpm brushes | 200 | 220 | 240 | 3 |
| Brakes | Yes | No | - |  |
| Speed (km/h) | 4,5 – 1,5 | 4,3km/h (4 working) | 4,3 km/h | 1 |
| On board charger | Yes | No | No |  |
| Water lift | 1250 mm/H2O | - | - | 2 |

COMPARISON SHEET – E71 vs TENNANT T5 and FIMAP SMX 75 BT

| NOTE N. | FEATURES / BENEFITS |
| --- | --- |
| 1 | The cleaning width combined to an higher working speed, allows a bigger productivity. |
| 2 | An optimal squeegee width combined to an excellent water lift, allow a impeccable floor drying. |
| 3 | The right brush pressure combined to an excellent RPM and a bigger water flow grant an excellent floor cleaning without efforts. |
| 4 | The aspiration engine class M filter protects it from damages due to the powder, reducing the maintenance. |
| 5 | A better climbing rate grants a more comfortable use in any kind of location. Either during the usage of the machine either during its transportation. |
| 6 | With its incredibly low noise level, the E71 is the ideal machine to work in any kind of location at any time. |
| 7 | The automatic brushes connection is an essential option to accelerate the cleanup and facilitate the use of the machine. |