## E75-2

PRODUCT Description

The model E75-2 it’s a professional ride-on scrubber-dryer, ideal for the cleaning of surfaces between 3.000 m² and 4.560 m².

With a cleaning width of 760mm and a speed of 6 km/h, this model boasts an area coverage of 4.560 m²/h.

Here after, the most important characteristics of this model:

- Strong anti-corrosion structure guaranteed several years;

- Rapid replacement of either brushes and pads without tools;

- Manually adjustable solution flow;

- Parabolic squeegee with a double adjustment, equipped with LINATEX blades to grant a perfect drying;

- Auto adjusting splash skirts to optimize the work on all type of floors;

- Electronic traction, infinitely variable;

- Solution level indicator;

- Very handy (1.560mm).

BRUSHES AND SQUEEGEE

- The E75 has a cleaning width of 760 mm, a squeegee width of 980 mm and boasts an area coverage of 4.560 m²\h.

- The brush pressure is 52kg.

- An electromagnetic valve starts the water flow slightly before the rotation of the brush or pad.

- The exclusive automatic brush connection system grants a very fast brush replacement.

- Brushing metal head equipped with protection wheels.

- The parabolic squeegee with double adjustment is equipped with LINATEX blades in order to grant an excellent drying.

- Dust filter situated in the internal part of the tank, it protects the aspiration engine from eventual hazardous waste and dust.

Applications

It is suitable to clean all paved floors, internal and external like: ceramic tiles, marble, cement, linoleum, porcelain tiles and with any kind of dirt.

- Factories

- Communities

- Schools

- Churches

- Hospitals

- Swimming pools

- Airports

- Locker rooms

- Commercial centres

- Logistic centres

- Cleaning companies

- Restaurants

standard ACCESSORIES

- WATER CUT-OFF ELECTROVALVE WHEN MACHINE IS TURNED OFF

- NO TOOLS, AUTOMATIC BRUSH COUPLING SYSTEM

- ADJUSTABLE PRESSURE AND INCLINATION SQUEEGEE

- SELF-LEVELING BRUSH DECK SEALING RUBBER

- BATTERY CHARGE INDICATOR WITH SAFETY POWER CUT-OFF

- StaINLESS STEEL FILTER

- SUPERELASTIC, NON-MARKING REAR TYRES

- MANUAL WATER FLOW DOSING

OPTIONAL AccessorIes

- WET TUBOLAR HEAVY DUTY BATTERIES 4 x (6V 180A IN C5)

- 6V BATTERY FITTING KIT

- GEL BATTERIES 6V (180 A IN C5) (4X)

- 2 X BRUSHES PPL 0,6

- 2 X BRUSHES PPL 0,9

- 2 X PAD HOLDERS

- 2 X BRUSHES TYNEX 1,2

- INOX SQUEEGEE (WITHOUT BLADES)

- SST (Stainless Steel Version)

- EDSS (Eureka Detergent Saving System)

TRACTION

The E75 uses the following type of traction:

ELECTRONIC, with START & STOP system

BATTERY CHARGER

The batteries charger is a standard equipment on the two versions.

To charge the batteries just plug the cable into an outlet of 220V with the machine off. It is better to turn off the machine before making this type of operation, if it was not the case, a safety mechanism automatically shut off the machine when inserting the plug and then it will turn it on once the plug is disconnected.

POWER SUPPLY

The E75 is available with the following batteries (optional):

  - Wet tubular heavy duty batteries : 4 x 6V (180 Ah)

  - Gel batteries : 4 x 6V (180 Ah)

- they don’t need maintenance

- there is no exhalation gas during loading

- there is no acid dispersion

-    they are completely sealed (there is no hole for inspection)

The machine can be adapted to any kind of battery simply changing the charging type in the battery charger and the settings in the electronic card.

VACUUM ENGINE

The vacuum engine 24V - 550W – 25 Ah creates a depression of 1250 mm/ H20.

TANKS

The tanks are 2 : the solution tank (110L) and the recovery tank (125L).

The special design of the recovery tank and the big diameter draining pipe allow to empty completely the dirty water, IN A VERY SHORT TIME, without leaving any type of rest and without manual interventions

COMPARISON CHART – E75 VS NILFISK BR 752 and HAKO TB 750

| MAIN FEATURES | E75 | NILFISK BR 752 | HAKO TB 750 |
| --- | --- | --- | --- |
| Cleaning width | 760mm | 710mm | 750mm |
| Squeegee width | 980mm | 890mm | 950mm |
| Steel plate squeegee | Yes | - | Yes |
| Brush pressure | 31kgs | 32-50kgs | - |
| Naked machine weight | 228kgs | 177kgs | 345kgs |
| Productivity | 3.572 m²/h | 2.980 m²/h | 4.800 m²/h |
| Climbing rate working | 10% | - | - |
| Climbing rate transferring | 20% | 16% | 10% |
| Brushes n° | 2 | 2 | 2 |
| Tanks capacity | 110 l – 125 l | 80l – 80l | 116 l - 116 l |
| Aspiration filter | Yes | Yes | Yes |
| Noise level | 68dB | 60dB | 75,4dB |
| Water flow (l/m) | 0-3,5 | 0-3 | 5,5-3,5 |
| Rated power | 2.050W | 2.320W | 3.260W |
| Automatic brush connection | Yes | Yes | Yes |
| Automatic splash skirt | Yes | No | Yes |
| Reverse speed | Yes | Yes | Yes |
| Brush speed | 190 | 230 | 200 |
| Brakes | Yes | Yes | Yes |
| Speed (km/h) | 4,7 – 2,5 | 6 | 6,5-3,4 |
| Water lift | 1250 mm/H2O | - | - |
| Direct transmission on the brush | Yes | No | - |
| Easy adjusting squeegee | Yes | Yes | - |
| Hermetic battery charger | Yes | Yes | Yes |
| Autonomy max | 2H30 | 1H45 | 1H15 |
| Installed batteries | 4 x 6V 180Ah | 4 x 6V 180Ah | 4 x 6V 180Ah |
| Traction engine metal protection bar | Yes | No | No |

COMPARISON CHART – E75 VS FIMAP MR75B and RCM ELAN 732

| MAIN FEATURES | E75 | MR75B | ELAN 732 |
| --- | --- | --- | --- |
| Cleaning width | 760mm | 750mm | 730mm |
| Squeegee width | 980mm | 990mm | 960mm |
| Steel plate squeegee | Yes | No | No |
| Brush pressure | 31kgs | 30kgs | - |
| Naked machine weight | 228kgs | 223kgs | 229kgs |
| Productivity | 3.572 m²/h | 4.500 m²/h | 3.650 m²/h |
| Climbing rate working | 10% | - | - |
| Climbing rate transferring | 20% | 18% | 10% |
| Brushes n° | 2 | 2 | 2 |
| Tanks capacity | 110 l – 125 l | 110l – 125l | 95 l - 100 l |
| Aspiration filter | Yes | Yes | Yes |
| Noise level | 68dB | - | - |
| Water flow (l/m) | 0-3,5 | - | - |
| Rated power | 2.050W | 1.610W | 1.280W |
| Automatic brush connection | Yes | Yes | Yes |
| Automatic splash skirt | Yes | No | No |
| Reverse speed | Yes | Yes | Yes |
| Brush speed | 190 | 170 | 185 |
| Brakes | Yes | Yes | Yes |
| Speed (km/h) | 4,7 – 2,5 | 6 | 5,5-3,5 |
| Water lift | 1250 mm/H2O | - | - |
| Direct transmission on the brush | Yes | - | - |
| Easy adjusting squeegee | Yes | Yes | - |
| Hermetic battery charger | Yes | Yes | Yes |
| Autonomy max | 2H30 | 2H15 | 2H45 |
| Installed batteries | 4 x 6V 180Ah | 4 x 6V 180Ah | 4 x 6V 180Ah |
| Traction engine metal protection bar | Yes | No | No |