## EC51

PRODUCT DESCRIPTION

The model EC51 is a professional escalator cleaner, ideal for the cleaning of areas between 0 m² and 2000 m².

With a cleaning width of 510mm, this model boasts an area coverage of 1.000 m²/h.

EC51 is equipped with a revolutionary cleaning system which is composed by a rotating head (180°) with two counter-rotating brushes.

Here after, the most important characteristics of this model:

- Strong anti-corrosion structure guaranteed several years;

- Exclusive rotating head system;

- It works independently even when the operator is not present;

- It can be used as a traditional floor cleaner;

- EC51 is standard equipped with a full range of tools to clean any part of the escalator.

BRUSHES AND SQUEEGEE

- The EC51 has a cleaning width of 510 mm, a squeegee width of 870 mm and boasts an area coverage of 1.000 m²\h.

- The brush pressure is 30kgs.

- Rotating head (180°) with two counter rotating brushes.

- Parabolic squeegee with a double adjustment, equipped with LINATEX blades to grant a perfect drying;

Applications

It is suitable to clean any kind of escalator, travelator and, in floor scrubber mode, can be used to clean large moquette surfaces and any kind of floor, exactly like a traditional scrubber dryer.

standard ACCESSORIES

- 02 - BRUSH Ø 115 X 510 mm TYNEX (TO BRUSH )

- 02 - BRUSH Ø 115 X 510 mm NYLON 0,25 (TO CLEAN)

- SQUEEGEE mm 870 ANT. / POST.

- SPRAY GUN

- SPIRALE PIPE

- VACUUM ASPIRATION PIPE

- BOX FOR BRUSHES CLEANING

- DUST FILTER

- COMPLETE MANUAL ACCESSORIES

POWER SUPPLY

The EC51 is available with the following power supply:

- V/Hz	230/ 50-60

ASPIRATION ENGINE

The aspiration engine 1.200W creates a depression of 2100 mm/ H20.

TANKS

The tanks are 2 : the solution tank (35L) and the recovery tank (35L).

The special design of the recovery tank and the big diameter draining pipe allow to empty completely the dirty water, IN A VERY SHORT TIME, without leaving any type of rest and without manual interventions.

COMPARISON SHEET – EC51 vs KARCHER BR 47/35 ESC and DUPLEX ESCALATOR 550 BASE

| MAIN FEATURES | EC51 | KARCHER BR 47/35 ESC | DUPLEX 550 BASE | NOTES |
| --- | --- | --- | --- | --- |
| Cleaning width | 510mm | 470mm | 620mm | 1 |
| Aspiration width | 510mm | 470mm | 620mm |  |
| Squeegee dimensions | 870mm | Not available | Not available | 2 |
| Brush pressure | 30kgs | - | - |  |
| Naked machine weight | 96kgs | 90kgs | 39kgs |  |
| Productivity | 1000 m²/h | - | - | 1 |
| Brushes n° | 1 | 1 | 1 |  |
| Tanks capacity | 35 l – 35 l | 35 l – 35 l | 9,5 l – 5,5 l | 1 |
| Rated power | 2.226W | 1900W | 1.900W |  |
| On board vacuum cleaner | Yes | No | No | 4 |
| Rotating head (180°) | Yes | No | No | 1 |
| Automatic work | Yes | No | No | 3 |
| Rpm brushes | 400 | - | - |  |
| Brakes | Yes | No | No |  |
| Water lift | 2100 mm/H²O | - | - |  |
| Floor scrubber mode | Yes | No | No | 2 |
| Carpet cleaning | Yes | No | No | 2 |
| Brushes automatic cleaning | Yes | No | No |  |

COMPARISON SHEET – EC51 vs NILFISK BA 531 and IPC CT 40 BT 55

| NOTE N. | FEATURES / BENEFITS |
| --- | --- |
| 1 | The cleaning width combined with a generous tanks capacity and the rotating head, allows a better productivity. |
| 2 | The EC51 is a very versatile machine, can be used to clean escalators, travelator, large carpeted areas and any kind of surface, thanks to the possibility to be used as a traditional scrubber-dryer. |
| 3 | The EC51 can work automatically, once it is positioned on the escalator it doesn’t need the operator support. |
| 4 | The on board vacuum cleaner gives a further support to the perfect cleaning of any surface. |