## KOBRA

PRODUCT DESCRIPTION

The KOBRA is a new walk-behind sweeper ideal for the fast, efficient sweeping of medium size areas.

Our major aim was to design an innovative machine, fast and productive, that could be sold at a very competitive price.

It is available either driven by a petrol engine (Honda ) or battery powered.

The battery version, which is extremely quiet and pollution free, is particularly suitable for indoor applications.

The KOBRA has a main brush of 550 mm, a total sweeping path of 780 mm, and boasts a working capacity of 3.510 m²\h.

The most relevant feature regards the collection of dust: in fact, fine dust is filtered through a polyester bag filter  (class USG), which allows for an excellent filtering rate ( 99,9% ) and has a much longer lasting life than traditional filters. The filter can be cleaned thanks to an efficient mechanical shaker.

Furthermore, the price of the KOBRA will enable users with a small budget to acquire the efficiency of a self-driven sweeper at a price they can justify and afford.

SWEEPING/VACUUMING SYSTEM

| KOBRA has a main brush width of 550 mm, a total sweeping path of 780 mm and a cleaning capacity, at full speed, of 3.510 m²\h. |  |
| --- | --- |
| The unit operates on the overthrow principle, i.e. debris are thrown over the cylindrical brush into the waste container situated behind it. |  |
| Traction can be activated by mean of a comfortable lever positioned on the operator’s handle. |  |
| A bulk waste flap is installed in front of the brush and easily operated from the controls handle. It allows the broom to pick up even bulkier debris. |  |
| The vacuum fan can be activated or deactivated by the mean of a control located on the dashboard. The standard right side brush can also be activated or deactivated from the dashboard. |  |

| Fine dust is filtered through a polyester bag filter ( class USG), which allows an excellent filtering rate ( 99,9% ) and has a much longer lasting life than traditional filters. The filter can be cleaned thanks to an efficient mechanical shaker. |  |
| --- | --- |
| The container has a real capacity of 40 Lt. and is mounted on wheels. It also has a convenient transport handle that allows the entire hopper to be rolled to the dump site. |  |
| The handle is adjustable to allow a better ergonomic and greater maneuverability, as it can be adapted to the height of the operator. |  |

| The body of the machine is made-up of a special anti-shock material to protect the KOBRA from unwanted damage. |  |
| --- | --- |
| Visibility is excellent from the operator’s position, and all controls are simple and ergonomically located for easy operation. |  |
| Maintenance access is convenient as well. The top lifts up to expose the engine\battery compartment as well as motors and other service areas. |  |

MAJOR APPLICATIONS AND TARGET GROUPS

KOBRA is particularly suitable for the cleaning of indoor/outdoor hard surfaces as well as large carpeted areas. It may also be suitable for a number of outdoor applications.

- Food industry

- Trucking and warehousing

- Paper and allied products

- Chemical industry

- Cleaning contractors

- Shopping malls

- Car parks

- Large hotel areas

- Lumber and wood products

- Service stations

- Airports ( indoor areas )

- Breweries

Standard solid rubber tyres allow unlimited operations in areas with glass or metal splinters.

Working time is, depending on the version, between 3-5 hours. This enables the KOBRA to sweep between 10.530 and 17.550 sq.mt (based on theoretical cleaning capacity).

SELLING FEATURES

* POLYESTER BAG FILTER, CLASS USG

* FLAP LIFT CONTROL

* HOPPER MOUNTED ON WHEELS

* ANTI-SHOCK BODY

* ADJUSTABLE HANDLE

* FULL RUBBER TIRES

* VACUUM-FAN CUT-OFF

* MULTI-BRISTLES MAIN BRUSH

*  BACK LOADING SYSTEM

* VERY COMPACT SIZE FOR MAXIMUM MANEUVERABILITY IN NARROW SPACES

*  DRIVE ON REAR WHEELS

* SIMPLE CONTROLS

* EXCELLENT VISIBILITY

* STRONG METAL STRUCTURE, COATED WITH EPOXY POWDER

* EASY ACCESS FOR SERVICING

* VERY COMPETITIVE PRICE!!

STANDARD ACCESSORIES

* POLYESTER BAG FILTER

* CONTROL PANEL INCLUSIVE OF :

STARTING KEY - VACUUM CUT-OFF CONTROL - SIDE BRUSH RAISING CONTROL

* CHEVRON TYPE MAIN BRUSH IN PPL, MIXED BRISTLES, Ø 265 X 550 mm

* SIDE BRUSH, PPL Ø mm 450

* TRACTION LEVER

* BODY MADE-UP OF ANTI-SHOCK MATERIAL

* HINGED HOOD IN SHOCK-ABSORBING MATERIAL

* FLAP RAISING DEVICE

* DIRT CONTAINER MOUNTED ON WHEELS, CAPACITY 40 Lt.

* ADJUSTABLE HANDLE

* PARKING BRAKE

* OIL LEVEL GAUGE

* MANUAL STARTER

* MECHANICAL FILTER SHAKING SYSTEM

* OIL CHECK DEVICE FOR HONDA VERSION

OPTIONAL ACCESSORIES

* CARPET CLEANING KIT

* REFUSE BOXES KIT

* HOURMETER KIT

* POLYESTER BAG FILTER- CLASS “USGC”

COMPARISON NOTES – KOBRA VS. KARCHER KM 75/40  – ISAL PB 55  – RCM BRAVA - IPC 512

| 1. MAJOR CHARACTERISTICS | KOBRA ST\ET | KARCHER KM 75/40 | ISAL PB 55 | NOTES |
| --- | --- | --- | --- | --- |
| Cleaning path only main broom | mm 550 | mm 550 | mm 500 | 1 |
| Cleaning path main broom + 1 side broom | mm 780 | mm 750 | mm 680 | 2 |
| Max. speed | 4,5 Km/h | 4,5 Km/h | 3,9 Km/h | 3 |
| Max. cleaning capacity | 3.500 m²\h | 3.375 m²\h | 2.700 m²\h | 4 |
| Capacity of dirt container ( volume ) | 40 Lt. | 40 Lt. | 36 Lt. |  |
| Dirt container mounted on wheels | YES | NO | NO | 5 |
| Loading system | Rear | Rear | Front |  |
| Flap lift | YES | NO | NO | 6 |
| Anti-shock body | YES | NO | NO | 7 |
| Multi-bristles main brush | YES - STANDARD | NO | NO | 8 |
| Type of filter | Polyester bag | Round panel | Panel | 9 |
| Filter shaking system | Mechanical | Mechanical | Mechanical |  |
| Type of drive ( ST H ) | Honda engine – 4 hp | Honda engine – 4 hp | Honda engine – 4 hp |  |
| Type of drive ( ET ) | Battery driven ( 12V – 105 Ah ) | Battery driven (12V) | Battery driven (12V) |  |
| 1. MAJOR CHARACTERISTICS | KOBRA ST\ET | RCM BRAVA HT\ET | IPC 512 | NOTES |
| Cleaning path only main broom | mm 550 | mm 510 | mm 500 | 1 |
| Cleaning path main broom + 1 side broom | mm 780 | mm 655 | mm 700 | 2 |
| Max. speed | 4,5 Km/h | 3,9 Km/h | 3,5 Km/h | 3 |
| Max. cleaning capacity | 3.500 m²\h | 2.600 m²\h | 2.450 m2\h | 4 |
| Capacity of dirt container ( volume ) | 40 Lt. | 40 Lt. | 50 Lt. |  |
| Dirt container mounted on wheels | YES | NO | NO | 5 |
| Loading system | Rear | Rear | Rear |  |
| Flap lift | YES | NO | NO | 6 |
| Anti-shock body | YES | NO | NO | 7 |
| Multi-bristles main brush | YES - STANDARD | NO | NO | 8 |
| Type of filter | Polyester bag | Panel | Panel | 9 |
| Filter shaking system | Mechanical | Mechanical | Mechanical |  |
| Type of drive ( ST H ) | Honda engine – 4 hp | Honda engine – 2,5 hp | Honda engine – 4 hp |  |
| Type of drive ( ET ) | Battery driven ( 12V – 105 Ah) | Battery driven (12V) | Battery driven (12V) |  |

COMPARISON NOTES – KOBRA VS. KARCHER KM 75/40  – ISAL PB 55  – RCM BRAVA - IPC 512

| NOTE NUMBER | FEATURE\BENEFIT |
| --- | --- |
| 1\2\3\4 | The larger main brush combined to a larger overall sweeping path and a faster operational speed, allows for an overall larger working capacity and productivity. |
| 5 | The KOBRA’S hopper is mounted on wheels and has a convenient transport handle that allows the entire hopper to be rolled easily to the dump site. |
| 6 | A bulk waste flap is installed in front of the brush and easily operated from the controls handle. It allows the broom to pick up even bulkier debris. |
| 7 | The body of the machine is made-up with an exclusive, special anti-shock material to protect the KOBRA from unwanted damage. |
| 8 | Integrated in the same brush are: a fine bristle section for fine dust and a thicker bristle section for heavier dust. KOBRA’s unique system allows for efficient performances on most floor\dirt types. |
| 9 | KOBRA is equipped with a polyester bag filter which is particularly efficient for the retaining of fine dust, and has a much longer lasting life than other traditional filters. Our competitor machines offer a single panel filter system which has disadvantages such as rapid clogging and dust coming out from the filter seals. |